## Slide 1: Heart Rate Monitor with the Arduino
Jens Gansloser
Fabian Meyer
SS14 – Ubiquitos Computing Mini-Project

## Slide 2: Project
Create a Heart Rate Monitor with the Arduino.
Advantages against commercial devices:
Full source code available
Full insight into the used technology
Can be compared to commercial ones in precision and performance
Higher performance/precision?

## Slide 3: Measurement Principle
Light reflected
Light through skin
LED (Red/IR)
Photodiode
Skin
Blood
Blood

## Slide 4: Heart Rate and Oxygen Saturation
Red LED (660nm)
IR LED (940nm)
Rate: time between two maxima / minima
Saturation: difference between red and infrared light intensity
Detect maxima / minima and calculate time difference.

## Slide 5: Hardware
Adafruit TSL Light Sensor
  Broadband and IR Photodiode
  Different integration times
  Different sensitivity
  I2C interface
Red and IR LED
Bluetooth Module (not used)
Arduino
  Needs I2C and USART support
Notes: 16bit resolution.

## Slide 6: Data Flow
Heart rate calculation
Arduino
Bluetooth module
Light sensor
I2C
UART
PC / Smartphone
Heart rate
Oxygen saturation
Heart rate (bpm)
Notes: Bluetooth not support, because we got a wrong module (not compatible to pc).
However, adding bluetooth support is easy (serial connection).

## Slide 7: Data Flow
Implementation not trivial: Prototype implemented on PC
Arduino
Light sensor
I2C
UART
PC
Heart rate
Light Sensor Data
Heart rate calculation
Notes: We implemented the prototype on the PC, for easier debugging and optimization. Our first aim was to get the heart rate.

## Slide 8: Software
QSerialPort
  Serial port control
FFTW
  Calculation of the Fourier Transform
Qt
  Graphical User Interface
Qwt
  Graphs
GUI
  Debugging and information display
Serial Interface
  Get sensor data
  Get sensor settings
  Set sample rate
FFT Module
  Signal processing
Arduino Software
  Read sensor light value (extended driver)
Libraries
Heart Rate Monitor

## Slide 9: Signal Processing
Output signal from the light sensor (array of discrete light values):
How to get the Heart Rate ( = Minima time difference)?
Pulse (with noise)
Notes: Output signal from light sensor (broadband photodiode)
Visualized on PC
Now how to get the pulse from this data?
Minima need to be determined.
Noise: Not clear curves, Y-axis shift.

## Slide 10: First Approach
Determine the grade
Is it declining or rising?
Determine minima
Notes: Wie kann man die minima bestimmen?

## Slide 11: First Approach
Determine the grade
Is it declining or rising?
Determine minima
Does not work!
Input light signal contains a lot of noise, a lot of shifting in the Y-Offset, different environment light, …

## Slide 12: Fourier Transform
Discrete Signal
Frequencies
Elegant way to determine the heart rate
Transform
Peak Frequency = Heart Rate
Notes: Beter and more elegant. After reading tons of books.
We want to find the frequency of the pulse.
 The frequency with the highes amplitude is the pulse (sinus frequency)

## Slide 13: Fourier Transform
Transform
. . . . . . . .
Filtering, Window Function, Zero Padding, …
Unfortunately not that easy …
Discrete Signal
Frequencies

## Slide 14: Which Fourier Transformation?
Complex, Real?
Discrete, Continues?
Periodic, Aperiodic?
 Complex Discrete Fourier Transform (DFT) - Forward transform synthesis (polar form)
Different application fields
N samples
x[n] discrete input values
X[k] discrete output values
Calculation with complex numbers

## Slide 15: Complex DFT
Input values
  Array of complex data (discrete input data)
  Real part = Sensor values
  Complex part = 0
Output values
  Array of complex data (discrete output data)
  Rectangular coordinate system (complex and real values – cos and sin functions)
  Transformation to polar coordinate system with magnitude and phase (human readable)
Notes: FFT = Fast Fourier Transform = Fast DFT Implementation
So lets see, what we have to give as input and get as output.

## Slide 16: Signal Processing
Filter
Window Function
FFT
Converting/
Scaling
Zero Padding
Notes: As already mention, we can not use only the FFT. We need to prepare the data at first
Here are the steps that need to be done to get a nice frequency spectrum at the end..

## Slide 17: Signal Processing
Butterworth Bandpass Filter
(Convolution)
 Remove unwanted frequencies
Hamming-Window
 Reduces Leakage Effect
Time Domain 
Frequency Domain
Interpret Output Array,
Prepare data,
Remove DC offset,
Find peak frequency, convert to bpm
Filter
Window Function
FFT
Converting/
Scaling
Zero Padding
Pad additional samples with zero 
Interpolation (for higher frequency resolution)
Notes: I will not explain these steps in detail. I only show the principle and why they need to be done.
Leakage effect is DFT related. Its when the sampled values don’t fit to the sinusoid basis frequency.
It makes the plot worse and harder to find the correct optimum.

## Slide 18: Signal Processing
Frequency Spectrum
No Filter and no Window Function
Notes: Lets see how these steps affect the resulting frequency spectrum.
Here are a lot of low frequencies which are not interesting end pollute the resulting spectrum.

## Slide 19: Signal Processing
Frequency Spectrum
No Window Function
Notes: Looks better but the peaks do not look very nice.

## Slide 20: Signal Processing
Frequency Spectrum
With everything
Notes: Nice smooth curve and peaks are easy to determine.

## Slide 21: Signal Processing
Frequency Spectrum
No Zero Padding
Notes: Results in lesser output points with lower frequency resolution. The peaks are not at their real x position.
Can be between two points.
However, the data is the same.

## Slide 22: Signal Processing
Output array of complex DFT (N samples)
(after converting to polar form)
[0]
[N/2]
[N-1]
Nyquist frequency
(1/2 of sample rate)
DC Offset (not displayed)
[1]
Peak
Peak
First data element
Peak detection only with this data
Notes: It is important, to correctly interpret the output data.

## Slide 23: Signal Processing
A lot of things to consider:
  Sample Frequency (Nyquist-Shannon theorem)
  Segment Duration
  Which Filter?
  Filter Parameters
  Target Frequency
  Filter stabilization time
  Correct data scaling
  Zero Padding (interpolation) – numer of samples
  Find correct frequencies
  Improving frequency resolution
  Number of samples
  Timeinterval for doing FFT
  …
Notes: Sehr viele Parameter zum Einstellen, sehr viele Schritte um Daten vorzubereiten.
Zu viel um alles zu erklären, deswegen ein paar hier aufgezählt.

## Slide 24: Further Steps / Improvement
Port to Arduino
  FFT library is available - http://wiki.openmusiclabs.com/wiki/ArduinoFFT
  Research needed, if performance is enough
  Else do signal processing on smartphone
Use smaller uC (ATtiny, …)
Add bluetooth module (trivial)
Add oxygen saturation measurement (easy to implement - the technology is the same as the heart rate measurement)
Create wrist band (smaller LED)
Brighter LED (to get greater frequecy peaks)
Notes: Vergleichstest durchgeführt – Messwerte sehr genau.

## Slide 26: Sources
http://www.dspguide.com/
Mastering the Discrete Fourier Transform in One, Two or Several Dimensions - Pitfalls and Artifacts, Isaac Amidror, Springer
DFT – Diskrete Fourier-Transformation, André Neubauer, Springer
Signaltheorie, Alfred Mertins, Springer
http://www.thefouriertransform.com/series/fourier.php
https://ccrma.stanford.edu/~jos/mdft/
http://paulbourke.net/miscellaneous/dft/
http://www.ignaciomellado.es/blog/Measuring-heart-rate-with-a-smartphone-camera
http://www-users.cs.york.ac.uk/~fisher/mkfilter/trad.html

## Slide 28
Forward FT
Inverse FT
Time
Domain
Frequency Domain

## Slide 29
real data
data vector (queue)
ptr = add(value)
effectiveSize
fftw_complex array
complex data
zeroPadding . . .
effectiveSize + zeroPadSize
copyToDataOut()

## Slide 30
Add data
Calculate FFT
Sliding Window

## Slide 31
Red LED
Luminosity Sensor
Finger is placed
between LED and
sensor

## Slide 33
Window Function
FFT
Ideal Filter
Zero Padding
Converting/
Scaling

## Slide 34
Light reflected
Light through skin
LED (Red/IR)
Photodiode
Skin
Blood
Blood